## Slide 1: virmlab – What’s new
Ulf Carlberg
Public, open source software available for download at:
https://dl.dropboxusercontent.com/u/13700179/virmlab.zip
2016-01-27

## Slide 2: Major Changes
Angles are given in degrees (not radians), both as inputs and internally in functions.
  Easier to interpret for humans.
  180 deg is exact, pi is approximated.
  Often ASCII data files use degrees.
  Matlab have functions that can handle degrees (sind, atan2d, …).
Waves, positions, and antennas are defined in slightly different structures (see next slides).
Channel matrix H is calculated with certain dimensions, see next slides.
Code is placed in several folders, see next slides.

## Slide 3: “Struct” for Waves, Antennas
w =
env_type: '3D'
N: 10000
Nw: 20
Ntx: 4
pol_type: 'LP'
K: []
theta_min: 0
theta_max: 180
phi_min: 0
phi_max: 360
theta: [10000x20x4 double]
phi: [10000x20x4 double]
Eth: [10000x20x4 double]
Eph: [10000x20x4 double]
a =
type: 'farfield'
name: 'inc. electric dipole'
actions: {'gen_farfield('inc. electric dipole', 19, 37)'}
freq: -1
Nth: 19
Nph: 37
Nfreq: 1
theta: [19x1 double]
phi: [37x1 double]
Eth: [19x37 double]
Eph: [19x37 double]
pow_rad: 12.5350
(0-180)
(0-360)
(complex)
(complex)

## Slide 4: “Struct” for Positions, Channel matrix
p =
N: 2
Na: 1
x: [2x1 double]
y: [2x1 double]
z: [2x1 double]
alpha: [2x1 double]
theta: [2x1 double]
phi: [2x1 double]
H: [1x4x2x10000 double]
Nrx = numel(a)
Ntx = w.Ntx
Npositions = p.N
Nrealizations = w.N
Typically, Nrx and Ntx is small (1-8) and Npositions and/or Nrealizations are large. The code is optimized for this.

## Slide 5: Folder Structure
demo – example input files (replaces example*.m)
doc – documentation files (text, Word, PowerPoint)
main – main source code functions. This folder should be added to Matlab’s path (once)!
test – test functions for verifying source code functions. Also useful as example of how to use various functions.
Create your own folders with your own files…