## Slide 1: virmlab – A Matlab tool for Antenna and Propagation Environment Analysis
Ulf Carlberg
Public, open source software available for download at:
https://dl.dropboxusercontent.com/u/13700179/virmlab.zip
Introduction and implementation details

## Slide 2: Introduction to virmlab
Abbreviation of ”Visual Random Multipath Laboratory”.
Implemented in Mathwork’s Matlab (no extra toolboxes needed).
Input is given in Matlab scripts. (More general and flexible than GUI.)
Output is presented as Matlab plots (2D and 3D).
Can simulate plane waves incident on antenna far-fields.
Example environment: RIMP – Rich Isotropic Multipath
Another example: RLOS – Random Line-of-sight
Not a full wave solver. Far-fields are imported from measurements or full-wave solvers such as CST and HFSS. Embedded far-fields can be imported for antenna arrays with several ports.

## Slide 3: Antenna Far-Fields (Import from Simulations or Measurements)
demo/meas_pattern.m

## Slide 4: Fading Statistic in Multi-Path Environments
demo/nice_illustration_Ez.m
demo/power_allocation.m

## Slide 5: Other Features
Rotation/translation of antennas far-fields
Plane wave incidents to antenna, or antenna-to-antenna coupling
Statistics of fading environments
Diversity/MIMO algorithm fading mitigation
Big arrays of antennas
Well-written and commented code with help section for each function
https://dl.dropboxusercontent.com/u/13700179/virmlab.zip

## Slide 6: Use “lookfor” command to find functions

## Slide 7: Study the Source Code with “edit” command

## Slide 8: Use “help”/”doc” command, or press F1 in editor

## Slide 9: Structured Programming
Follows “MATLAB Programming Style Guidelines” by Richard Johnson
  http://www.datatool.com/downloads/matlab_style_guidelines.pdf
Modularized
  The program consist of many small (max two editor screens/100 lines) well-designed functions.
  Any block of code never appear in more than one place.
Commented
  Help section in beginning of functions.
  Comments that explain why and how something is done in the code.
Tested
  Test scripts included for many functions.

## Slide 10: Main Capabilities of Simulation Tool
Generate a rich multipath environment by a number of incoming plane waves that are
  Random uniformly distributed over 4π or
  Random only from azimuth or
  Any other distribution of interest
Sample the fields/calculate port voltage for
  Dipoles, Huygen’s sources, pencil beams of cosn(θ/2)-shape etc
  Any antenna (from CST, HFSS, measurements)
Gather samples by
  Walking in a path or
  Generate new incoming waves or
  Distribute users

## Slide 11: Further Capabilities of Simulation Tool
Plot and animate
  Waves
  Fields
  CDF
  etc
Place two or more antennas close to each other and calculate MED, correlation, capacity, diversity gain
  Compare different environments (Uniform/Azimuth)
  Compare number of incoming waves
  Compare orientation in non-uniform environments
Matlab Scripts as input to give maximum flexibility for the user

## Slide 12: “Struct” for Waves, Antennas
w =
env_type: '3D'
N: 10000
Nw: 20
Ntx: 4
pol_type: 'LP'
K: []
theta_min: 0
theta_max: 180
phi_min: 0
phi_max: 360
theta: [10000x20x4 double]
phi: [10000x20x4 double]
Eth: [10000x20x4 double]
Eph: [10000x20x4 double]
a =
type: 'farfield'
name: 'inc. electric dipole'
actions: {'gen_farfield('inc. electric dipole', 19, 37)'}
freq: -1
Nth: 19
Nph: 37
Nfreq: 1
theta: [19x1 double]
phi: [37x1 double]
Eth: [19x37 double]
Eph: [19x37 double]
pow_rad: 12.5350
(0-180)
(0-360)
(complex)
(complex)

## Slide 13: “Struct” for Positions, Channel matrix
p =
N: 2
Na: 1
x: [2x1 double]
y: [2x1 double]
z: [2x1 double]
alpha: [2x1 double]
theta: [2x1 double]
phi: [2x1 double]
H: [1x4x2x10000 double]
Nrx = numel(a)
Ntx = w.Ntx
Npositions = p.N
Nrealizations = w.N
Typically, Nrx and Ntx is small (1-8) and Npositions and/or Nrealizations are large. The code is optimized for this.
Nfreq

## Slide 14: Folder Structure
demo – example input files (replaces example*.m)
doc – documentation files (text, Word, PowerPoint)
main – main source code functions. This folder should be added to Matlab’s path (once)!
test – test functions for verifying source code functions. Also useful as example of how to use various functions.
Create your own folders with your own files…

## Slide 15: Waves from random directions with random amplitude, phase and polarization
Uniform:

## Slide 16: Waves from random directions with random amplitude, phase and polarization
From azimuth only:

## Slide 17: Units
SI-units unless otherwise specified, so the variable freq implies a unit in Hertz and the variable freq_GHz is given in GHz.
Angles are normally given in degrees! (Often supplied in measurement files, easier to interpret, can express e.g. 90 degrees and 180 degrees exactly with floating point numbers.)

## Slide 18: Coordinate Systems used in virmlab
The usual Cartesian ”xyz”-coordinates.
Spherical coordinates r, theta, phi, where theta is measured from the z-axis.
Do not use Matlab’s cart2sph() or sph2cart()! They use different definitions (and radians). Use the functions rthetaphi2xyz() and xyz2rthetaphi().

## Slide 19: How to Interpret Results: CDF curves
“1 per cent of samples are -30 dB below threshold or worse”
Good curves to the right!

## Slide 20: Probability of Detection (PoD)
Good curves to the left!
“To be able to detect 95 % of users, we need an average power 22 dB over the threshold level.”